## Slide 1: Air pollution

## Slide 2: Lead in gas
Purpose of tetraethyllead was to prevent premature ignition in engines, allowing higher pressures to be used
Released lead particles into the atmosphere
Inhaled lead impairs brain development in children
As of 2021 it is now banned in all countries

## Slide 3: Acid rain
Historically dominated by sulfur dioxide, but limits on sulfur content of fuels has dramatically helped
  Combines with other things in atmosphere to form sulfuric acid
Now nitrogen dioxide is also becoming important
  Combines with other things in the atmosphere to form nitric acid
Can have PH as low as about 4
Dissolves or corrodes some building materials
Toxic to plants and animals

## Slide 4: CFCs (image: pubchem)
Widely used as refrigerants, degreasing agents, and aerosol propellants
  Non-toxic
  Non-flammable
  Non-reactive
Low reactivity meant long environmental half life
  Allows them to reach stratosphere
Reacts with ozone, destroying it
Also strong greenhouse gases
Example CFC shown here:

## Slide 5: CFC ozone breakdown details
Note: the photon must be high energy UV, almost exclusive to upper atmosphere

## Slide 6: Replacing CFCs: HCFCs and HFCs
Producing CFCs is now banned, the only source is recycling of old devices.
HCFCs are less stable than CFCs and thus exhibit less ozone depletion potential
HFCs are completely free of ozone depletion potential, but most are still extremely potent greenhouse gases
HCFCs are being phased out around the world

## Slide 7: Replacing HCFCs and HFCs
Problems with alternatives
  Carbon dioxide
    requires very high pressures to be efficient
  HFC-152a (a particular HFC)
    still a greenhouse gas, but much less so
    Mildly flammable
  Ammonia
    Toxic
    Mildly flammable

## Slide 8: Sulfurous smog (aka London Type)
Results from mix of sulfur dioxide with fog
Also involves particulate matter
Less of a problem than in the past due to sulfur dioxide regulations

## Slide 9: Photochemical Smog (aka Angeles Type)
Combustion of fossil fuels produces VOCs and nitrogen dioxide

## Slide 10: Some notes
ToxicStuff includes PANs, which are major respiratory irritants, mutagens and carginogens
We don’t really care about the ‘stuff’ in the last reaction.

## Slide 11: Indoor air pollution: Carbon Monoxide
Carbon monoxide
  Exists in small amounts in the body and functions as a neurotransmitter
  Produced by incomplete combustion
    natural gas burning appliances
    Cars left running in garages
  Heavier than air
  Acutely toxic because it binds with hemoglobin, interfering with oxygen delivery
  Sometimes causes permanent hearing damage on acute or chronic exposure. There is no scientific consensus on the mechanism.

## Slide 12: Indoor Air Pollution: VOCs
Glues used in furniture
Solvents
Paint
Carpet, vinyl flooring
Air fresheners

## Slide 13: Indoor Air Pollution: Modern buildings
Modern buildings are very well sealed to improve insulation
Allows for buildup of chemicals in the air
No way for radon to escape