## Slide 1: Environmental History and Legislation

## Slide 2: The state of things before legislation
TEL is almost universal in gasoline
  Prevents premature detonation, allowing for higher compression
    Improves fuel economy slightly
    Improves vehicle performance substantially
  Toxicity of lead was somewhat known since antiquity
    Nicander documented poisoning from lead carbonate in his poetry (circa 200 BCE)
    Pliny the Elder documented toxicity of lead fumes (circa 50 CE)
    Dioscorides documented the toxicity of some lead compounds when eaten (circa 70 CE)

## Slide 3: State before legislation 2
Cuyahoga River had caught fire several times (probably 14 according to most sources), with little attention until the famous 1969 fire
Kent State Forum 1968: From 1,000 feet [300 m] below Lower Harvard Bridge to Newburgh and South Shore Railroad Bridge, the channel becomes wider and deeper and the level is controlled by Lake Erie. Downstream of the railroad bridge to the harbor, the depth is held constant by dredging, and the width is maintained by piling along both banks. The surface is covered with the brown oily film observed upstream as far as the Southerly Plant effluent. In addition, large quantities of black heavy oil floating in slicks, sometimes several inches thick, are observed frequently. Debris and trash are commonly caught up in these slicks forming an unsightly floating mess. Anaerobic action is common as the dissolved oxygen is seldom above a fraction of a part per million. The discharge of cooling water increases the temperature by 10 to 15 °F [5.6 to 8.3 °C]. The velocity is negligible, and sludge accumulates on the bottom. Animal life does not exist. Only the algae Oscillatoria grows along the piers above the water line. The color changes from gray-brown to rusty brown as the river proceeds downstream. Transparency is less than 0.5 feet [0.15 m] in this reach. This entire reach is grossly polluted.

## Slide 4: State before legislation 3
Lead pipes became relatively common starting in mid 1800s
In 1900 roughly 70% of cities in USA had lead pipes, including nearly all major cities
Toxicity was known and documented, concerns from physicians, researchers were ignored in favor of ease of installation
Lead industry was able to lobby to keep lead based pipe installation

## Slide 5: The beginning 1899
Rivers and harbors act makes it block streams or discharge refuse into waters
  Regarded as first environmental legislation in USA
  Initially concerned only with garbage that would interfere with boat traffic (without a permit)
  Later interpreted to include industrial wastes

## Slide 6: Air pollution control act (1955)
Leaves actual control up to states
Authorizes/funds research into air pollution

## Slide 7: EPA Creation
Nixon gave a list of environmental recomendations to Congress in 1970. These included:
  Asking for national air quality standards/emission regulations
  Asking for end to dumping in Great Lakes
  Asked for 4 billion dollars for improvement of water treatment facilities
  The establishment of a national agency to oversee these and other regulations (EPA)

## Slide 8: EPA authority
Research pollutants
Monitor condition of environment
Set limits for specific pollutants (shared authority with states)

## Slide 9: Clean air act
Technically the 1963 act was the one titled the clean air act, but a 1970 act is also usually referred to as the clean air act
Regulates motor vehicle emissions, prevents states from setting more strict regulations
  Exception for California due to major smog issues. In practice this means that California dictates motor vehicle emission laws.

## Slide 10: NAAQS
Ozone
PM2.5/PM10
Lead
CO
SOx
NOx
EPA must set standards for all these pollutants

## Slide 11: Has been amended several times.
1990 H.W. Bush asked for increased regulatory ability to address acid rain, urban pollution and toxic emissions
Granted by house and senate, additional provisions added for phaseout of ozone depleting substances (notably CFCs) as in the Montreal protocol.
Established cap-and-trade system for dealing with sulfur dioxide
  Would later be expanded to NOx compounds as well
  Many have argued for cap-and-trade on carbon dioxide as well

## Slide 12: 1977 amendments
Air that already meets standards cannot be allow to deteriorate
Stricter automobile emissions standards
Signed by Carter

## Slide 13: Carter’s work
Large sections of Alaska made into permanent preserves
Championed renewable energy
  Famously put solar panels on the white house
Fought back against industry control of regulation
Cancelled many dam projects based on environmental concerns

## Slide 14: Water pollution control act (1948) aka clean water act and early regulations
Provided some basic regulations for navigable waterways
Provided states with authorization to limit pollutants
Almost completely replaced by 1972 amendment, this is what people mean when they say clean water act or water pollution control act

## Slide 15: 1972 “Clean water act”
Wastewater standards may be set by EPA
Point source pollution is controlled: EPA delegates permitting to states
  Subsequent case law has included an idea of equivalence to direct discharge

## Slide 16: Legal challenges
Many legal challenges have been filed against the clean air and clear water acts both by industries and by environmentalists